# Gst-sh-mobile-enc
Gst-sh-mobile-enc – encodes raw YUV image data to MPEG4/H264 video stream on SuperH environment using libshcodecs HW codec.
# Synopsis
Gstshvideoenc;
# Object hierarchy
Gobject
  - GstObject
    - GstElement
      - Gstshvideoenc
# Properties
“cntl-file”	string	: Read / Write
# Description
This element is designed to use the HW video processing modules of the Renesas SuperH chipset to encode MPEG4/H264 video streams. This element is not usable in any other environments and it requires libshcodes HW codec to be installed.
The encoding settings are defined in a control file, which is given to the encoder as a property.
## Example launch line
gst-launch filesrc location=test.yuv ! gst-sh-mobile-enc cntl-file=m4v.ctl ! filesink location=test.m4v
# Synopsis
## Element information
Plugin	gst-sh-mobile
Author	Johannes Lahti <johannes.lahti@nomovok.com>
Class	Codec/Encoder/Video

## Element pads
Name	Sink
Direction	Sink
Presence	Always
Details	video/x-raw-yuv, format=(fourcc)NV12, width=(int)[48,720], height=(int)[48,576],	framerate=(fraction)[1,25]
video/x-raw-yuv, format=(fourcc)NV12, width=(int)[48,720], height=(int)[48,480],	framerate=(fraction)[1,30]

Name	Source
Direction	Src
Presence	Always
Details	video/mpeg, width=(int)[48,720], height=(int)[48,576], framerate=(fraction)[1,25],	mpegversion=(int)4
video/mpeg, width=(int)[48,720], height=(int)[48,480], framerate=(fraction)[1,30],	mpegversion=(int)4
video/x-h264, width=(int)[48,720], height=(int)[48,576], framerate=(fraction)[1,25],	h264version=(int)h264, variant=(string)itu
video/x-h264, width=(int)[48,720], height=(int)[48,480], framerate=(fraction)[1,30],	h264version=(int)h264, variant=(string)itu
# Details
## Gstshvideoenc
typedef struct _Gstshvideoenc Gstshvideoenc;
Opaque data structure.
# Property details
## The “cntl-file” property
“cntl-file”	string	: Read / Write
Name of the encoding control file.
Default value: NULL